## Slide 1: CSCI E-25 Computer Vision
Steve Elston
Copyright 2022, 2023 Stephen F Elston. All rights reserved.
Convolution and Image Filtering

## Slide 2: Image Filtering
Almost all computer vision pipelines require filtering
Without good image data preparation even the most state of the art CV algorithms will not produce good results
Classical filters apply the mathematical operation of convolution
  Noise suppression
  Edge and corner enhancement
  Anti-aliasing
We can understand the effects of filtering through spectral analysis
  Filter changes power spectrum of image
  Typical filters reduce high-frequency energy – noise
  Higher frequency components include sharp edges and corners – typically blurred by filtering

## Slide 3: Image Filtering
Key points for this lesson
The Fourier transform and frequency components of images
How convolution works in 1-d, 2-d and higher dimension
How to apply padding, stride and tiling for convolution
Constructing convolutional filter kernels
The relationship between filtering and the spectrum of images

## Slide 4
The Fourier Transform

## Slide 5: Decomposition of Images by Frequency Components
Fourier Transform decomposes a series of values into its frequency components
We can understand the effect of filters on an image by comparing power spectrums
The Fourier transform maps a sequence of values to a set of frequency coefficients
  The Fourier coefficients are complex numbers:
  For our purposes, we care about the power spectrum coefficients

## Slide 6
Convolution

## Slide 7: Convolution
Convolution operations are a computationally efficient method of applying filters
Convolutional kernel weights determine characteristics of filter
  Filtering noise
  Creating and enhancing features
Convolutional filtering computationally efficient
  High volume applications
  Real-time CV

## Slide 8: Convolution
Convolution operations are a computationally efficient method of applying filters
Discrete convolutional kernels have a span, measured in points
Kernel moves over image, a stride length at a time, producing filtered output
Typically stride span
Tiled filters do no overlap, stride = span

## Slide 9: Convolution
Convolution operations are a computationally efficient method of applying filters to discretely
Convolution kernel is moved along the input tensor
  Kernel has a small span compared to dimension of input tensor
  Number of kernel dimensions number of input tensor dimensions
  At each step a weighted output value is computed
  Output tensor can have different number of dimensions from input tensor
1-D convolutions are a simple, but useful example
  Time series data
  Text data
  Speech

## Slide 10: 1-D Convolution
1-D CNNs are a simple, but useful example
Consider a convolutional kernel with a span of 3 and stride 1
Kernel defined by weights
The convolved value is the weighted sum over the span of the convolutional kernel
W1
W2
W3
t = 3
Kernel Span
or
Receptive Field

## Slide 11: 1-D Convolution
1-D CNNs are a simple, but useful example
Move kernel by stride 1
The convolutional kernel moves one sample per step
t = 4
Kernel Span
or
Receptive Field
W1
W2
W3

## Slide 12: 1-D Convolution
1-D CNNs are a simple, but useful example
Continue to produce one output value per time step
t = 5
Kernel Span
or
Receptive Field
W3
W1
W2

## Slide 13: 1-D Convolution
1-D CNNs are a simple, but useful example
Convolution ends when end of series reached
Output is , shorter than original series
t = n
Kernel Span
or
Receptive Field
W1
W2
W3

## Slide 14: 1-D Convolution
Mathematically, express 1-d convolution as a weighted sum over a set of discrete kernel values:
Where:
the output of the convolution operation at time t
series of values
convolution kernel
convolution operator
time difference of the convolution operator
, for odd length operator

## Slide 15: 2-D Convolution
Input
Output
4 x 4 input tensor
3 x 3 convolution operator
2 x 2 output tensor

## Slide 16: 2-D Convolution
Mathematically, we express 2-d convolution as a weighted sum over a discrete rectangular kernel:
Where S, I and K are now 2-dimensional tensors

## Slide 17: 2-D Convolution
The image and kernel tensors are commutative in the convolution relationship
This allows an operation known as kernel flipping with the following alternative result:

## Slide 18: Convolution in Higher Dimensions
Tensor notation allows easy extension to higher dimensions
  Input tensor has multiple input channels
  3-D for color image
  4-D for video
Create multiple feature maps
  Convolution kernel tensor has multiple output channels
  Each output channel is a different feature map
  Feature in a channel might be vertical lines, horizontal lines, corners, etc

## Slide 19: Algebraic Properties of Convolution
Convolution operations have useful algebraic properties
Notice that these properties are identical to the familiar algebraic properties of multiplication
Name | Property
Commutativity | 
Associativity | 
Distributivity | 
Associativity of scalar multiplication | 
Name | Property
Commutativity | 
Associativity | 
Distributivity | 
Associativity of scalar multiplication | 

## Slide 20
Stride, Tiling and Padding for Convolution

## Slide 21: Stride and Tiling
Do we always move the convolution kernel by 1 data value?
No!
  May not need the full resolution of the input
  Or, change the dimension of the input tensor
Stride > 1 down-samples the data
  Output of lower resolution
Stride < 1 up-samples the data
  Output of higher resolution
Stride can be fractional to create the required output dimension

## Slide 22: Stride and Tiling
Input
Output
Stride
Stride
Tiling is a special case when stride = span:
Stride >1 reduces dimensionality

## Slide 23: Padding for Convolution
How can we best deal with edges of the input tensor when performing convolution?
A valid convolution confines the kernel to the input tensor dimensions
  For odd kernel shape, output dimension is (span + 1)/2 less than input dimension
  After many convolution layers, dimension is reduced further
We can zero pad the input tensor
  Dimensionality is maintained

## Slide 24: Padding for Convolution
Input
Output
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
Convolution
Operations
Dimension of output tensor = dimension of input tensor
0 values have little effect with max pooling
Example: 4x4 input tensor with 3x3 kernel

## Slide 25
Commonly Used Convolution Kernels

## Slide 26: Common Convolution Kernels
A moving average kernel has equal weights
Example, a 3 x 3 moving average kernel
This is also known as a blur filter or box blur
Notice the normalization so weights add to 1.0

## Slide 27: Common Convolution Kernels
A Gaussian kernel smooths an image
Weights computed from Gaussian function with span parameter :
Example, a 3 x 3 Gaussian kernel,
Then Gaussian kernel limits the bandwidth and blurs the image
The smaller the span (larger s) of the Gaussian kernel the narrower the bandwidth

## Slide 28: Common Convolution Kernels
The Sobel kernel takes the first derivative of the image
Compute the partial derivatives of the image, , along each axis
Here, , is the convolution operator
Notice the sum of the weights is 0
Other derivative kernels can be derived

## Slide 29: Common Convolution Kernels
The Sobel kernel is an example of a separable kernel
Notice that we can write a Sobel kernel as the product of two 1-dimensional kernels
For computational efficiency a 2-dimensional separable kernel can be applied as the convolution of 2 1-dimensional kernels

## Slide 30: Median Filter
Median filter is a special case
Median filter outputs median value of the pixel values within patch
  Typically use odd patch sizes – e.g., 3 x 3, 5 x 5, 7 x 7
Median filter is not easily formulated using convolution
  Use an incremental update algorithm for computational efficiency
Median filter has interesting properties
  Suppresses noise
  Sharpens edges and corners
Median filter can alter image
  Response is not isotropic – not same along diagonals of image
  Can move edges and corners

## Slide 31
Filtering and Spectral Properties of Images

## Slide 32: Spectral Properties of Images
The power spectrum of an image reveals fundamental properties
Power spectrum reveals the vertical and horizontal frequency components of the image
Low frequency components of an image represent regions with slowly changing properties
High frequency components of an image arise from local features with rapid changes
  Edges
  Corners
  Texture
Filtering changes the power spectrum of an image

## Slide 33: Spectral Properties of Images
We can decompose an image into frequency components using a Fourier transform
The Fourier transform decomposes a signal into frequency components
The 1-dimensional Fourier transform of a function, , can be expressed:
is the complex spectrum of
  Real component is the frequency
  Imaginary component is phase at frequency
  Magnitude of the complex number is the signal amplitude at frequency

## Slide 34: Spectral Properties of Images
We can decompose an image into frequency components using a Fourier transform
The Fourier transform decomposes a signal into frequency components
is the complex spectrum of
  Real component is the frequency
  Imaginary component is phase at frequency
  Magnitude of the complex number is the signal amplitude at frequency
Amplitude
Credit, Wikipedia commons
Two sinusoidal signals with identical frequency and amplitude, phase shifted by q

## Slide 35: Spectral Properties of Images
Example of single frequency signals and their spectrum

## Slide 36: Spectral Properties of Images
Example of signal with two frequencies and the spectrum

## Slide 37: Spectral Properties of Images
Impulse response of convolutional a filter is the Fourier transform in the frequency domain
Fourier Transform
Filter in time domain
Filter in frequency domain
Relationship is reversable (inverse Fourier transform) and commutable – exchange time and frequency domain
Credit, DSP Illustrations

## Slide 38: Spectral Properties of Images
Impulse response of some commonly used convolutional filters
Name of the filter
Values of the kernel operator
Analytical representation of the Fourier transform
Graph of the Fourier transform or impulse response
Credit: Szeliski, 2nd Edition

## Slide 39: Spectral Properties of Images
For a discretely sampled image we use a 2-dimensional discrete Fourier transform
The discrete Fourier transform is sampled over image samples (pixels), , and discrete frequencies, , within the Nyquist limit:
( )
  is the spatial index of a discrete pixel
  are discrete horizontal and vertical frequencies
Notice the limited spatial range of the sampling
  Not
  Limited spatial sampling introduces edge artifacts – edges of images are impulses

## Slide 40: Spectral Properties of Images
The power spectrum of an image reveals fundamental properties
Spectral density reveals the power or energy in vertical and horizontal frequency components of the image
In words, the spectral density is the lag-1 autocorrelation of the estimated Fourier transform,
Or square of the absolute value of the estimated Fourier transform

## Slide 41: Spectral Properties of Images
The power spectrum of an image reveals fundamental properties
Spectral density reveals the power or energy in vertical and horizontal frequency components of the image given the estimated Fourier transform,
Spectral density is easier to work with, since it just gives us the power at each frequency, w
  The squared magnitude of the signal at w
Notice that, unlike Fourier transform, the spectral density is not invertible
  The square of absolute magnitude of loses phase information

## Slide 42: Spectral Properties of Images
For real-valued image, spectral density is symmetric about zero frequency
Rapid changes (e.g. edges, corners) have high frequency components
Vertical frequency = 0
Spectral density reveals the power or energy in vertical and horizontal frequency components of the image
Horizontal frequency = 0
Increasing vertical frequency
Increasing vertical frequency
Increasing Horizontal frequency
Increasing Horizontal frequency

## Slide 43: Spectral Properties of Images
Filters change the spectral characteristics of images
Filters can suppress unwanted high frequency noise
Filtering reduces aliasing
Lower frequency image is blurred – edges and corners less sharp
Changes in spectral density show the effect of filtering
Gaussian Filter
s = 1.0

## Slide 44: The Convolution Theorem
There is a direct relationship between filtering in the spatial (or time) domain and the frequency domain, the convolution theorem
For spatial domain image, , its Fourier transform, , operating on by a spatial domain convolutional kernel, , its Fourier transform, , we can state the convolution theorem:
In words, the convolution theorem states that convolution in the spatial domain is equivalent to the inverse Fourier transform of the point wise product in the frequency domain, or vice versa
The convolution theorem helps us understand the effects of filtering

## Slide 45: Summary
Key points for this lesson
How convolutional works in 1-d, 2-d and higher dimension
How to apply padding, stride and tiling for convolution
Constructing convolutional filter kernels
The relationship between filtering and the spectrum of images