## Slide 1: CSCI E-25 Computer Vision
Steve Elston
Copyright 2021, 2022, 2023, 2024 Stephen F Elston. All rights reserved.
Homography and Projections

## Slide 2: Homography and Projections
How do we transform between light scattered off objects and projections on a camera image plane?
Use planar projective transformation to model projection of an object to a camera image plane
Use projection to transform one camera pose to another
Inverse transform from image planes to real-world object location
Planar transformations use projection matrix

## Slide 3: Homography and Projections
Projections are used in many computer vision applications
Warping images to adjust for camera viewpoint, aka, camera pose
Tracking moving objects – a.k.a. optical flow
Stitching images together
3D computer vision
Integrating different imaging types, e.g. lidar and optical – beyond scope of our course
…

## Slide 4: Stereo Vision Problem
Stereo vision is a canonical problem in computer vision
Can locate a point in 3-D space from location on 2 or more image planes
Requires a model for the cameras
  Intrinsic properties of cameras
  Scene extrinsic from cameras
Solve system of camera equations to locate point in 3-D space
w
x1
x2
Image plane 2
Image plane 1
Optical center 2
Optical center 1

## Slide 5: Image alignment
Example: How to align images from two views?
Locate interest points
For patches around the interest points extract statistics - descriptors
Matching points are identified by descriptors
Images can be warped to match – use image transformations
B1
B2
B3
A1
A2
A3

## Slide 6: Pinhole Camera Model

## Slide 7: Pinhole Camera
Pinhole camera is a canonical model for image formation
First known description by Chinese philosopher Mo Ti (Mozi) in 5th Century BCA
Described by Greek philosopher Aristotle in 4th century BCA
Known in Europe as Camera Obscura from about the 10th Century
Pinhole camera is a chamber with a small hole on one side

## Slide 8: Pinhole Camera
Pinhole camera is a canonical model for image formation
Pinhole camera is a chamber with a small hole on one side
Image on side of chamber opposite hole
Use cartesian coordinates on the image plane
Pinhole is the origin of the coordinate system
Transform from real-world coordinates to image plane coordinates

## Slide 9: Coordinate Systems

## Slide 10: Cartisian Coordinates for Images
Pinhole camera model
O
Image plane,
Optic Axis, z
Pinhole at origin
Object
Image
Principal Point

## Slide 11: Pinhole Camera
Pinhole camera is a canonical model for image formation
3-D real-world position translates to x-y position on image plane
Positions are defined relative to the optic axis,
Optical center, , is origin of coordinate system
x-y image plane position, , changes with optical center coordinates:
  - horizontal location with respect to optic axis
  - vertical location with respect to optic axis
  - distance from pin hole along the optic axis
Pinhole camera image inverted

## Slide 12: Coordinate System for Pinhole Camera
Images are formed on an image plane
Place image plane between pin hole, origin, and object
  Image no longer inverted
  Simplifies transformations
Real-world and image plane coordinate along optic axis measured from optic center
Distance from origin to image plane is focal length,
  Simplify model by setting

## Slide 13: Pinhole Camera Model
Cartesian coordinates for a pinhole camera model
O
Image plane,
Optic Axis = z
Pinhole at origin
Principal Point

## Slide 14: Cartesian Coordinates for Images
Transform homogenous coordinates to cartesian coordinates
Transform from real-world to image plane coordinates
distance from origin to object
With focal length , and w = distance from origin to image plane:
are all measured in real-world units, e.g. mm

## Slide 15: Focal Length
Short focal length
Long focal length
Field
of
view
Field
of
view
Changing focal length changes field of view a fixed distance
w
w
Image plane
Image plane

## Slide 16: Transformations for Camera Model

## Slide 17: Transformations for Camera Model
Transform formations applied using pin hole camera model
Transformation between real-world and image coordinates require two sets of parameters
Intrinsic or camara parameters,
  – focal length
  – image array offset
  – skew correction, or idiosyncratic term
Extrinsic or object position and orientation parameters
  – Rotation matrix
  - translation

## Slide 18: Transformations for Camera Model
Extrinsic transformation for position and orientation of object
Extrinsic transformation comprised of two independent operations
Rotation transformation,
The complete extrinsic transformation is then:

## Slide 19: Transformations for Camera Model
Intrisic transformation adjusts for characteristics of a camera
Intrinsic transformation comprised of three independent components
  Focal length,
  Image array offsets,
  Skew correction,
Intrinsic or Camera calibration matrix,
  And

## Slide 20: Transformations for Camera Model
Complete transformation accounts for image placement and camera characteristics
Linear extrinsic and intrinsic transformations combined by matrix multiplication:
These equations are no longer linear
  depends on and vice versa!
Estimating the parameters requires solving a nonlinear optimization problem

## Slide 21: Transformations for Camera Model
How do we find the Intrinsic parameters of a camera?
Two ways to find intrinsic parameters
  Learn from multiple camera views of scene – more on this later
  Use multiple views of a known target
Wide variety of targets available commercially
Other suppliers

## Slide 22: Homogeneous Coordinates

## Slide 23: Homogenous Coordinates
Can form linear system of equations in homogenous coordinates
Define position on image plane and object:
Transform back to Cartesian image plane coordinates,

## Slide 24: Pinhole Camera Model
Homogenous coordinates for a pinhole camera model
O
Image plane,
Optic Axis
Pinhole at origin
Principal Point

## Slide 25: Homogenous Coordinates
Extrinsic transformation represented by a single matrix combining rotation and translation:
The complete extrinsic transformation in homogeneous coordinates:
A set of linear equations!

## Slide 26: Homogenous Coordinates
How can we construct the intrinsic transformation in homogenous coordinates?
  And
  A set of linear equations!

## Slide 27: Homogenous Coordinates
How to solve for the constant ?
In homogenous coordinates we can solve the three equations to find :

## Slide 28: Pinhole Camera Model in Homogeneous Coordinates
Homogenous coordinates for a pinhole camera model
O
Image plane,
Optic Axis
Pinhole at origin
Principal Point

## Slide 29: Four Transformation Problems

## Slide 30: Four Transform Problems
How can we simplify these planar transformations?
There are four levels of complexity
2-D Euclidean – Rotation and translation
2-D Similarity – Rotation, translation, and scaling
Affine - Rotation, translation, scaling, shearing
Projective – General transformation

## Slide 31: Four Transform Problems
How can we simplify these planar transformations?
Model is restricted to planar transformations
Transformation matrices are constant over image
Assumes all objects in image are at a constant distance from image plane
How to overcome the limitations of the model?
  Can apply transformations over patches of the image
  Or, use a polynomial representation of parameters

## Slide 32: Four Transformations
2-D Euclidean transformation
Planer operation
Applies rotation and translation
3 degrees of freedom
  1 – rotation angle
  2 - translation
Simple cases
  Pure rotation – 1 DoF
  Pure translation – 2 DoF
Preserves shape, size , parallel lines

## Slide 33: Four Transform Problems
2-D Euclidean transformation – rotation and translation
Transformation from one 2-d plane to another can be defined in homogeneous coordinates
Multiply both sides by

## Slide 34: Four Transform Problems
2-D Euclidean transformation – rotation and translation
Can write the transformation in Cartesian coordinates
Or,

## Slide 35: Four Transformations
2-D Euclidean transformation
Pure rotation case:
1 DoF,
Right-handed coordinate system positive gives counter clockwise rotation

## Slide 36: Four Transformations
2-D Euclidean transformation
Pure translation case:
2 DoF,

## Slide 37: Four Transformations
2-D Euclidean transformation
Translation and rotation
3 DoF,

## Slide 38: Four Transformations
2-D similarity transformation
Planer operation
Applies rotation, translation and scale
4 degrees of freedom
  1 – rotation angle
  2 - translation
  1 - scale
Preserves – shape, parallel lines

## Slide 39: Four Transform Problems
2-D similarity transformation – rotation, translation and scale
Transformation from one 2-d plane distance D to another can be defined in homogeneous coordinates
With , a scale factor, and

## Slide 40: Four Transform Problems
2-D similarity transformation – rotation and translation
Can write the transformation in Cartesian coordinates
Or,

## Slide 41: Four Transformations
2-D similarity transformation
Translation, rotation and scale
4 DoF,

## Slide 42: Four Transformations
Affine transformation
Applies rotation, translation, scale and shear
6 degrees of freedom
  1 – rotation angle
  2 - translation
  2 – scale
  1 - shear
Preserves – parallel lines

## Slide 43: Four Transform Problems
Affine transformation – rotation, translation, scale and shear
Generalized affine transformation from one 2-d plane to another can be defined in homogeneous coordinates
In Cartesian coordinates, letting , the transformation is:

## Slide 44: Four Transform Problems
Affine transformation – rotation, translation, scale and shear
In Cartesian coordinates, letting , the transformation is:
Or,

## Slide 45: Four Transformations
2-D affine transformation
Translation, rotation, scale and shear
6 DoF,

## Slide 46: Four Transformations
Projective transformation or homography
Applies general transformation
8 degrees of freedom
Preserves – straight lines, but nothing else

## Slide 47: Projective Transform
Homogenous coordinates projective transform is the most general case
O
Image plane,
Optic Axis
Pinhole at origin
Principal Point

## Slide 48: Four Transform Problems
Projective transform or homography - general unrestricted transformation
General transformation plane to another can be defined in homogeneous coordinates
3,

## Slide 49: Four Transform Problems
Projective transform or homography - general unrestricted transformation
Continue with the matrix multiplication
3,
8 DoF, not all independent

## Slide 50: Four Transform Problems
Projective transform or homography - general unrestricted transformation
Starting with linear system of equations
Can find a solution in Cartesian coordinates:

## Slide 51: Four Transform Problems
Projective transform or homography - general unrestricted transformation
Can find a solution in Cartesian coordinates:
These are nonlinear equations!
Nonlinear relationship makes it hard to understand how parameters interact

## Slide 52: Four Transform Problems
Projective transform or homography - general unrestricted transformation
How can we interpret this transform?
Typically set and adjust
extrinsic translation in x, y, and z
But also x, y intrinsic offsets and scale,
rotation, scale, and shear, but dependent on intrinsic parameters terms , focal length and sensor skew

## Slide 53: Four Transform Problems
Projective transform or homography - general unrestricted transformation
How can we interpret this transform?
Intrinsic skew correction , dependent on extrinsic terms
What about ?
These off-diagonal extrinsic terms change camera pose
Effect of changing camera pose dependent on in intrinsic terms

## Slide 54: Summary
Planar transforms map between light scattered off objects and projections on a camera image plane
Planar projective transformation model based on pinhole camera
Use projection to transform one camera pose to another
Inverse transform from image planes to real-world object location
Planar transformations use projection matrix
  2-D Euclidean – Rotation and translation
  2-D Similarity – Rotation, translation, and scaling
  Affine - Rotation, translation, scaling, shearing
  Projective – General transformation