## Slide 1: CSCI E-25 Computer Vision
Steve Elston
Copyright 2021, 2022, Stephen F Elston. All rights reserved.
Homography and Projections

## Slide 2: Homography and Projections
How do we transform between light scattered off objects and projections on a camera image plane?
Use planar projective transformation to model projection of an object to a camera image plane
Use projection to transform one camera pose to another
Inverse transform from image planes to real-world object location
Planar transformations use projection matrix

## Slide 3: Homography and Projections
Projections are used in many computer vision applications
Warping images to adjust for camera viewpoint, aka, camera pose
Tracking moving objects – a.k.a. optical flow
Stitching images together
3D vision and stereo vision
Integrating different imaging types, e.g. lidar and optical
…

## Slide 4: Stereo Vision Problem
Stereo vision is a canonical problem in computer vision
Can locate a point in 3-D space from location on 2 or more image planes
Solving this problem requires a model for the cameras
Solve system of camera equations to locate point in 3-D space
w
x1
x2
Image plane 2
Image plane 1
Optical center 2
Optical center 1

## Slide 5: Image alignment
Example: How to align images from two views?
Locate interest points
For patches around the interest points extract statistics - descriptors
Matching points are identified by descriptors
Images can be warped to match – use image transformations
B1
B2
B3
A1
A2
A3

## Slide 6: Pinhole Camera
Pinhole camera is a canonical model for image formation
First known description by Chinese philosopher Mo Ti (Mozi) in 5th Century BCA
Described by Greek philosopher Aristotle in 4th century BCA
Known in Europe as Camera Obscura from about the 10th Century
Pinhole camera is a chamber with a small hole on one side
Image on side of chamber opposite hole
Use cartesian coordinates on the image plane
Pinhole is the origin of the coordinate system
Transform from real-world coordinates to image plane coordinates

## Slide 7: Homogenous Coordinates for Images
Pinhole camera model
O
Image plane,
Optic Axis
Pinhole at origin
Object
Image

## Slide 8: Pinhole Camera
Pinhole camera is a canonical model for image formation
3-D real-world position translates to x-y position on image plane
Positions are defined relative to the optic axis,
x-y image plane position, , changes with optic axis coordinates:
  - horizontal location with respect to optic axis
  - vertical location with respect to optic axis
  - distance from pin hole along the optic axis
Pinhole camera image inverted

## Slide 9: Coordinate System for Pinhole Camera
Images are formed on an image plane
Place image plane between pin hole, origin, and object
  Image no longer inverted
  Simplifies transformations
Real-world and image plane coordinate along optic axis
Optic axis from origin or optic center
Distance from origin to image plane is focal length,
  Simplify model by setting

## Slide 10: Pinhole Camera Model
Homogeneous coordinates for a pinhole camera model
O
Image plane,
Optic Axis
Pinhole at origin
Principle Point

## Slide 11: Cartesian Coordinates for Images
Transform homogenous coordinates to cartesian coordinates
Transform from real-world to image plane coordinates
distance from origin to object
With focal length, w , distance from origin to image plane:
are all measured in real-world units, e.g. mm

## Slide 12: Transformations for Camera Model
Transform formations applied using pin hole camera model
Transformation between real-world and image coordinates require two sets of parameters
Intrinsic or camara parameters,
  – focal length
  – image array offset
  – skew correction, or idiosyncratic term
Extrinsic or object position and orientation parameters
  – Rotation matrix
  - translation

## Slide 13: Transformations for Camera Model
Extrinsic transformation for position and orientation of object
Extrinsic transformation comprised of two independent operations
  Rotation transformation,
  Translation transformation,
The complete extrinsic transformation is then:

## Slide 14: Transformations for Camera Model
Intrisic transformation adjusts for characteristics of a camera
Intrinsic transformation comprised of three independent components
  Focal length,
  Image array offsets,
  Skew correction,
Intrinsic or Camera calibration matrix,
  And

## Slide 15: Transformations for Camera Model
Complete transformation accounts for image placement and camera characteristics
Linear extrinsic and intrinsic transformations combined by matrix multiplication:
These equations are no longer linear
Estimating the parameters requires solving a nonlinear optimization problem

## Slide 16: Homogenous Coordinates
Can form linear system of equations in homogenous coordinates
Define position on image plane and object:
And,

## Slide 17: Pinhole Camera Model
Homogenous coordinates for a pinhole camera model
O
Image plane,
Optic Axis
Pinhole at origin
Principle Point

## Slide 18: Homogenous Coordinates
Extrinsic transformation becomes a single matrix combining rotation and translation:
The complete extrinsic transformation in homogeneous coordinates:
A set of linear equations!

## Slide 19: Homogenous Coordinates
How to construct the intrinsic transformation in homogenous coordinates?
  And
  A set of linear equations!

## Slide 20: Homogenous Coordinates
How to solve for the constant ?
In homogenous coordinates we can solve the three equations to find :

## Slide 21: Transformations for Camera Model
How do we find the Intrinsic parameters of a camera?
Two ways to find intrinsic parameters
  Learn from multiple camera views of scene – more on this later
  Use multiple views of a known target
Wide variety of targets available commercially
Other suppliers

## Slide 22: Pinhole Camera Model in Homogeneous Coordinates
Homogenous coordinates for a pinhole camera model
O
Image plane,
Optic Axis
Pinhole at origin
Principle Point

## Slide 23: Stereo Vision Problem
Stereo vision is a canonical problem in computer vision
w
x1
x2
Image plane 2
Image plane 1
Optical center 2
Optical center 1
w
x1
x2
Image plane 2
Image plane 1
Optical center 2
Optical center 1
Mislocated object
Image misalignment
Located object
Image alignment

## Slide 24: Four Transform Problems
How can we simplify these planar transformations?
There are four levels of complexity
2-D Euclidean – Rotation and translation
2-D Similarity – Rotation, translation, and scaling
Affine - Rotation, translation, scaling, shearing
Projective – General transformation

## Slide 25: Four Transform Problems
How can we simplify these planar transformations?
Model is restricted to planar transformations
Parameters in the transformation matrices are constant over image
Single transformation for all pixels on the image
Assumes all objects in image are at a constant distance from image plane
Can apply transformations over patches of the image

## Slide 26: Four Transformations
2-D Euclidean transformation
Planer operation
Applies rotation and translation
3 degrees of freedom
  1 – rotation angle
  2 - translation
Simple cases
  Pure rotation – 1 DoF
  Pure translation – 2 DoF
Preserves shape, size , parallel lines

## Slide 27: Four Transform Problems
2-D Euclidean transformation – rotation and translation
Transformation from one 2-d plane to another can be defined in homogeneous coordinates
Multiply both sides by

## Slide 28: Four Transform Problems
2-D Euclidean transformation – rotation and translation
Can write the transformation in Cartesian coordinates

## Slide 29: Four Transformations
2-D Euclidean transformation
Pure rotation case:
1 DoF,
Right-handed coordinate system positive gives counter clockwise rotation

## Slide 30: Four Transformations
2-D Euclidean transformation
Pure translation case:
2 DoF,

## Slide 31: Four Transformations
2-D Euclidean transformation
Translation and rotation
3 DoF,

## Slide 32: Four Transformations
2-D similarity transformation
Planer operation
Applies rotation, translation and scale
4 degrees of freedom
  1 – rotation angle
  2 - translation
  1 - scale
Preserves – shape, parallel lines

## Slide 33: Four Transform Problems
2-D similarity transformation – rotation, translation and scale
Transformation from one 2-d plane distance D to another can be defined in homogeneous coordinates
With , a scale factor, and

## Slide 34: Four Transform Problems
2-D similarity transformation – rotation and translation
Can write the transformation in Cartesian coordinates

## Slide 35: Four Transformations
2-D similarity transformation
Translation, rotation and scale
4 DoF,

## Slide 36: Four Transformations
Affine transformation
Applies rotation, translation, scale and shear
6 degrees of freedom
  1 – rotation angle
  2 - translation
  2 – scale
  1 - shear
Preserves – parallel lines

## Slide 37: Four Transform Problems
Affine transformation – rotation, translation, scale and shear
Generalized affine transformation from one 2-d plane to another can be defined in homogeneous coordinates
In Cartesian coordinates the transformation is:

## Slide 38: Four Transformations
2-D similarity transformation
Translation, rotation, scale and shear
6 DoF,

## Slide 39: Four Transformations
Projective transformation or homography
Applies general transformation
8 degrees of freedom
Preserves – nothing

## Slide 40: Four Transform Problems
Projective transform or homography - general unrestricted transformation
General transformation plane to another can be defined in homogeneous coordinates
3,

## Slide 41: Four Transform Problems
Projective transform or homography - general unrestricted transformation
Continue with the matrix multiplication
3,
8 DoF, not all independent

## Slide 42: Four Transform Problems
Projective transform or homography - general unrestricted transformation
Starting with linear system of equations
Can find a solution in Cartesian coordinates:

## Slide 43: Projective Transform
Homogenous coordinates projective transform is the most general case
O
Image plane,
Optic Axis
Pinhole at origin
Principle Point

## Slide 44: Summary
Planar transforms map between light scattered off objects and projections on a camera image plane
Planar projective transformation model based on pinhole camera
Use projection to transform one camera pose to another
Inverse transform from image planes to real-world object location
Planar transformations use projection matrix
  2-D Euclidean – Rotation and translation
  2-D Similarity – Rotation, translation, and scaling
  Affine - Rotation, translation, scaling, shearing
  Projective – General transformation